## Slide 1
start
Take ultrasonic sensor QMC5883 magenetometer module as input
Take Arduino UNO for interfacing
Upload programming code to Arduino
Display output on monitor
Connect VCC and GND of sensor to Arduino 5v & GND
connect serial clock pin to analaog input pin A5 and serial data pin to analog input pin A4

## Slide 2
start
initialise trigger signal pin
initialise echo signal pin
if echo signal receives means there is obstacle ,buzzer immediately rings up
initialise buzzer as output
send trigger signal continuosly
read the staus of echo signal pin
check for echo signal if echo signal not receive then continue
yes
no

## Slide 3
start
Take joystick module as input
Take Arduino UNO for interfacing
Upload programming code to Arduino
Connect both servo motors black wire to Gnd and red wire to VCC also connect yellow wires of first motor to pin 8 and second motor pin 9
Take two servomotor as output
Connect VCC and GND of sensor to Arduino 5v & GND
Connect joystick modules VER pin to A0 and HOR pin to A1

## Slide 4
start
Initialise variables for two servo motors
initialise pin of joystick module and signal pin of servo motor
Declare vertical and horizontal pin pin on joy stick as input
read status of horizontal and vertical position input
check value of horizontal pos.
check value of vertical pos.
>700
<300
<300
>700
first servo motor
will move right
first servo motor
will move left.
second servo motor
will move left.
second servo motor
will move right

## Slide 5
start
Take PIR sensor as input
Take Arduino UNO for interfacing
Upload programming code to Arduino
Connect buzzer positive end to D13and negartive end to GND
Take buzzer and LED as output
Connect signal out pin sensor to the digital data input (D2)
Connect digital input pin 12 to cathode of LED

## Slide 6
start
Initialise PIR sensor as input pin and pin sensor to read values
initialise LED and Buzzer as output pin
define ports for sensor input ,led output and buzzer output
check output of motion sensor
LED ON
read output value of motion sensor
o/p=HIGH
o/p=LOW
LED OFF

## Slide 7
start
Take TTP223 Capacitive Touch Sensor
as input
Take Arduino UNO for interfacing
Upload programming code to Arduino
Connectservo motor supply voltage pin to Vcc and GND pin of Arduino and servo motor control signal pin to digital pin (D3)
Take servo motor and LED as output
Connect VCC and GND pin of sensor to arduino
Connect signal out pin of sensor to the digital input pin (D2)of Arduino.
Connect LED output pin to Digital pin 5 of arduino.

## Slide 8
start
Initialise variable for servo motor control signal
Initialise touch sensor signal as inputpin
rotate servo motor 0 degree to 180 degree
Initialise LED as output pin
Read output of touch sensor
Check output of touch sensor
r=high and p=low
r=low and p=high
rotate servo motor180 degree to 0 degree
waitw
wait

## Slide 9
start
Take 3 module of IR Sensor
as input
Take Arduino UNO for interfacing
Upload programming code to Arduino
connect the positive pin of leds to D8,D9,D10 pins of arduino.
Take LED as output
Connect VCC and GND pin of three sensor to Arduino board.
Connect signal out pins of sensor to the digital input pins (D2,D3,D4)of Arduino.
Ground pins of led connect to the ground of arduino.

## Slide 10
start
Define first sensor as IR1,second sensor as IR2,third sensor as IR3
define digital pins as outpin pin for LED
3. Initialse ports for IR sensor and LED
assign variable t1 to read value of IR1,t2 for IR2 and t3 for IR3
LED 1 ON
Check values of variables
t3=HIGH
Read values of variables
LED 2 ON
LED 3 ON
t1=HIGH
t2=HIGH

## Slide 11
start
Take 3 module of sound sensor
as input
Take Arduino UNO for interfacing
Upload programming code to Arduino
connect the positive pin of led to D5 pin of arduino.
Take LED as output
Connect VCC and GND pin of sound sensor to Arduino board.
Connect signal out pins of sensor to the digital input pins (D3)of Arduino.
Ground pins of led connect to the ground of arduino.

## Slide 12
start
Initialise Sound sensor as input pin and pin sensor to read values
initialise LED as output pin
define ports for sensor input , LED output
Initialise status sensor to read value of input sound sensor
LED ON
read value of status sensor of sensor
o/p=HIGH
o/p=LOW
LED OFF

## Slide 13
start
Take ultrasonic sensor HC-SR04
as input
Take Arduino UNO for interfacing
Upload programming code to Arduino
Connect servo motor supply voltage pin to Vcc and GND pin of Arduino and servo motor control signal pin to digital pin (D12)
Take servo motor as output
Connect VCC and GND pin of sensor to arduino
Connect trigger pin of sensor to the digital input pin (D10) and echo pin to D11 of Arduino.

## Slide 14
start
Defines Trigger and Echo pins of the Ultrasonic Sensor
Define Variables for the duration and the distance
if echo signal receives means there is obstacle , rotate servo motor
Sets the trigPin as an Output and Sets the echoPin as an Input pin
Defines on which pin is the servo motor attached
Define function for calculating the distance measured by the Ultrasonic sensor for each degree
check echo pin status
yes
Reads the echoPin returns the sound wave travel time in microseconds.
no

## Slide 15
start
Take ultrasonic sensor HC-SR04
as input
Take Arduino UNO for interfacing
Upload programming code to Arduino
Connect motor module supply voltage pin to Vcc and GND pin of Arduino and motor enable signal pinENA ,ENB to digital pin (D8&D11)
Take motor as output
Connect VCC and GND pin of sensor to arduino
Connect trigger pin of sensor to the digital input pin (A0) and echo pin to A1 of Arduino.
connect digital input pin IN1,IN2 to the 9 pin of arduino
And IN3,IN4 to the 10 pin of arduino

## Slide 16
start
Initialise constant integer to drive motor as IN1,IN2,IN3,IN4
Initialise trigger signal input pin as A4 and echo signal pin as A5
Move motor to the left
Define port for output and input
Read the status of echo signal pin
Measure the distance
If distance <30cm
yes
no

## Slide 17
start
Take force sensor
as input
Take Arduino UNO for interfacing
Upload programming code to Arduino
Display information on Arduino
Connect VCC and GND pin of sensor to arduino
connect analog input pin (A0) to negative end of sensor.

## Slide 18
start
Define integer variable for sensor input as A2
Define integer variable for sensor value
Read sensor value
Check values of variables
NO PRESSURE
NO PRESSURE
LIGHT TOUCH
LIGHT SQUEEZE
MEDIUM
SQUEEZE
STRONG
PRESSURE”
<10
<200
<500
<800
>800
Display pressure

## Slide 19
start
Take potentiometer
as input
Take Arduino UNO for interfacing
Upload programming code to Arduino
take LED as output
Connect VCC and GND pin of potentiometer to arduino
connect anode to digital pin6 to negative end of ground

## Slide 20
start
Initialise integer variable for LED pin
Initialise integer variable for potentiometer pin as A0
Initialise output variable and initialise led value as output variable
Read the value of potentiometer by vaiable led_value.
Display LED value

## Slide 21
start
Take MQ-2 gas sensor
as input
Take Arduino UNO for interfacing
Upload programming code to Arduino
take buzzer and LED as output
Connect VCC and GND pin of gas sensor to Arduino and analog pin of sensor to A5
connect positive end of buzzer to to digital pin10 and negative end to the ground
connect positive end of LEDs to to digital pin11 and 12 and negative end to the ground

## Slide 22
IN time:9.05
Recreated project report temperature &humidity sensor
Created enerfy conservation project
-wind mill
-solar power LED street light
Created flowchart
-touch control led
-rf transmitter recevr module
-password based security system
-led matrix
-destination notifier
-accelerometer
-air pollution monitoring
out time : 7.20